## Slide 1: ENGINEERING DESIGN 2026
GENERAL FEEDBACK

## Slide 2: MAIN CONTROL BOARD
Prototype successfully completed
SPWM implemented, 3 or 6 IO, 10 kHz switching freq
ADC ADS1220 on SPI
Port Expander 2x 8bit ports (15 usable)
uSD Card and RTCC support
RGB Status LED
At a glance

## Slide 3: MAIN CONTROL BOARD
Chinese Mid-Autumn Holiday period leads to factory shutdowns
Completion estimate is 4 October
In Production

## Slide 4: DELIVERY ESTIMATE 9 OCTOBER 2026
Boards arrive partially assembled.
Connectors must be soldered by individual groups.

## Slide 5: Interface protection

## Slide 6: WHY BOTHER
Products necessitates interfacing low-voltage and high voltage
  Inverter control
  General switching applications
  Field-bus transients
Dealing with transients
Fast
Potential for galvanic isolation
Very Fast (8us)
Alternative path provision
Slow
Galvanic isolation, direct mains switching

## Slide 7: OPTICAL ISOLATION
V2 via R1 supplies LED in U1
Transistor in U1 low side switch
L1 fed via V1
  No current limiting
Switching is limited to Vce max
Low Voltage Differentials

## Slide 8: SWITCHING LOADS
Ground is not perfect 0R
Distributed L and C induces voltage transients
3V MCU
  High 3V, Low 0V
  0.8V bounce > High 2.2V, Low -0.8V
2.2V nuisance sporadic behaviour
-0,8V input > Blown MCU
What happens to voltages…

## Slide 9: OPTICAL ISOLATION
MCU Loop (V2) completely isolated
Worst case V1 loop spike destroys U1
Correct usage

## Slide 10: A typical implementation
Shared GND offers no transient protection to MCU
U1 used as a voltage-level-translator
Very easy trap!
Poor isolation performance

## Slide 11: A typical configuration
Good Isolation Performance
ONLY IF PSU
PROVIDES
GALVANIC ISOLATION

## Slide 12: INCREMENT 2
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 8.2 | 3.2 | 1.4 | 1.2
Start to integrate aspects.
Even a single controlled MOSFET/IGBT is significant progress.